## Slide 1: Non-revisiting Coverage Task with Minimal Discontinuities for Non-redundant Manipulators
Tong Yang, Jaime Valls Miro, Yue Wang, Rong Xiong
Robotic Laboratory, Zhejiang University
Centre for Autonomous Systems (CAS), University of Technology Sydney
Robotics: Science and Systems 2020

## Slide 2: Problem
Given an object of arbitrary shaped, follow a path to completely traverse its surface with a non-redundant manipulator, whilst minimising the number of end-effector lift-offs.
Or the Non-revisiting Coverage Path Planning

## Slide 3: Previous Work Problem Modeling
Given known environment settings
Use colours to represent IK solutions
Model the problem as a graph colouring scheme
Solve the colouring problem
URL: https://arxiv.org/abs/2001.09577v1
Simple objects
Consider small set of task constraints
Thus overlook the existence of non simply-connected cells

## Slide 4: Previous Work Finiteness of Solving Simply-connected Cells
No need to have cutting path starting or ending at the middle of edges
No need to have intersecting cutting paths
No need to have cutting path stretching across edges
Only applicable for
simply-connected cells
URL: https://arxiv.org/abs/2001.09577v1

## Slide 5: Previous Work Simply-connected Cells – Cell Subdivision
For a simply-connected cell with edges, the number of divisions is
URL: https://arxiv.org/abs/2001.09577v1

## Slide 6: Contribution 1: Problem Modeling
The NCPP problem with least discontinuities can be modelled as a topological graph as long as:
A point contact between surface and the end-effector is assumed
Singular configurations and their neighbors can be discarded
Constraints are defined in joint-space with thresholds satisfying strict inequalities.
(See paper for further details and proof)

## Slide 7: Contribution 1: Problem Modeling Example of non Simply-connected Cells due to Collision
“Holes” in cells appear due to collision between manipulator and obstacle
Manipulator about to hit a “hilly terrain”
initial topological graph

## Slide 8: Contribution 1: Problem Modeling Example of non Simply-connected Cells due to Non-binary Metrics
High manipulability
(brighter color)
Low manipulability
(darker color)
Metric: configuration manipulability
Arbitrary metrics produce complex topological graphs.

## Slide 9: Contribution 1: Problem Modeling
Topological graphs with different manipulability thresholds
7
6
(Note: all wrist-flipped configurations become invalid)

## Slide 10: Contribution 2: A Systematic Solution of Topological Graphs
The structures of arbitrary-shape cells can be classified through their genus.
Solve iteratively:
Find and discard equivalent divisions genus-1 cells are finitely solvable.
Propose a three-stage solver for genus-2 cells with proven finiteness of divisions.
Present an -stage solver for genus- cells.
(See paper for details and complexity analysis)

## Slide 11: Contribution 2: A Systematic Solution of Topological Graphs Solution of Genus-1 Cells
Equivalence 1: Disconnected inner part is negligible.
①
②
+
=
=
=
=
=
=
Enforce connecting
cell 1 and cell 2
Unconnectable
area
All different divisions (having same cost)
Solve the graph without inner cell
Place the inner cell arbitrarily afterwards
②
①

## Slide 12: Contribution 2: A Systematic Solution of Topological Graphs Solution of Genus-1 Cells
Equivalence 2: The outer part is also negligible
From equivalence 1&2:
When inner part is disconnected, inner and the outer parts are independent.
A graph with a genus-1 cell
(area between two squares)
Projecting the original graph
onto sphere using
stereographic projection
Inner part and outer part interchange their roles

## Slide 13: Contribution 2: A Systematic Solution of Topological Graphs Solution of Genus-1 Cells
Equivalence 3: Negligibility of cyclic cutting paths
Only the acyclic situations requires explicit consideration.
Once an acyclic solution is optimal, equivalent cyclic solutions are all optimal.
cycles
cycle
cycle
cycles
=
=
=
=
=
=
a continuous transformation shows the equivalence
cycle
cycle
cycle
cycle
cycle
=
=

## Slide 14: Contribution 2: A Systematic Solution of Topological Graphs Solution of Genus-1 Cells
Equivalence 4: Negligibility of single cutting path
It is not the cutting path but a connected area that transforms a genus-1 cell into simply-connected sub-cells.
A contradiction
Connecting two inner cells
Connecting two outer cells
Two sides of a cutting path must have different colors, but they are the same cell!

## Slide 15: Contribution 2: A Systematic Solution of Topological Graphs Counter Example
Different structures shown by different sub-cells
Goal: enforce connection of cells 1, 3, 7, 10
Connected edges do not uniquely define the structure of the cutting paths

## Slide 16: Contribution 2: A Systematic Solution of Topological Graphs 2-Stage Process: Solution of Genus-1 Cells
Equivalence 5: The negligibility of cyclic cutting paths
Cutting paths that start and end at the same boundary (the red one) can be seen as further divisions
The third (and later) cutting paths connecting inner and outer boundary can be seen as further divisions
Hence, in stage 1, all required cutting paths are:
2 cutting paths connecting the inner and outer part
Consider a two-stage process:
Stage 1: The genus-1 cell is divided into simply-connected sub-cells
Stage 2: Create further divisions

## Slide 17: Contribution 2: A Systematic Solution of Topological Graphs Example of the Solving Process
Choose the edges connecting
Choose the edges connecting
We just show in which branch will cells 1, 3, 7, 10 be connected.
Let new indices in sub-cell be:
Let new indices in sub-cell be:
Stage 2: Further divisions
Stage 1: Transforming the genus-one cell to simply-connected cells
(See paper for list of all divisions)

## Slide 18: Contribution 2: A Systematic Solution of Topological Graphs 3-Stage Process: Solution of Genus-2 Cells
Genus-2 cell with outer boundary defined by , and inner boundaries
defined by :
Stage 1: Insert and create two cutting paths.
Stage 2: Insert and create two cutting paths (need further equivalence).
Stage 3: Create all further divisions.

## Slide 19: Contribution 2: A Systematic Solution of Topological Graphs 3-Stage Process: Solution of Genus-2 Cells
Hence, in stage 2, only two conditions need consideration:
In sub-cell 1 a new genus-1 cell with outer edges and inner edges
In sub-cell 2 a new genus-1 cell with outer edges and inner edges
Equivalence 6: Negligibility of putting inner part on the cutting paths
Stage 1 has finished
is not on cutting paths
is on cutting paths
and ② are connectable
non-optimal
( and ② are unconnectable)

## Slide 20: Contribution 2: A Systematic Solution of Topological Graphs -Stage Process: Solution of Genus- Cells
Genus- cell with its outer boundaries defined by , and inner boundaries
defined
Stage 1: Insert and create two cutting paths.
Stage : Insert to one of the sub-cells after stage
and create two cutting paths.
Stage : Create all sub-division cutting paths.

## Slide 21: Contribution 2: A Systematic Solution of Topological Graphs Example of -Stage Process
Init graph
Stage 1
Stage 2
Stage 3

## Slide 22: Experiment : Polishing a Mobiüs Strip
Find All
Configurations
The least number of discontinuities is 1
(note: the actual physical cutting
path is arbitrary.)
Define Colors
Create Topological
Graph
One of the Optimal
Solutions

## Slide 23: Experiment : Polishing a Mobiüs Strip
Going Through Discontinuity
First Section
Second Section

## Slide 24: Experiment : Polishing a Swimming Ring
Find All
Configurations
Define Colors
Create Topological
Graph
One of the Optimal
Solutions
The least number of discontinuities is 1
(note: the actual physical cutting
path is arbitrary.)

## Slide 25: Experiment : Polishing a Swimming Ring
Going Through Discontinuity
First Section
Second Section

## Slide 26: Experiment : Polishing a “Hilly Terrain”
Find All
Configurations
Define Colors
Create Topological
Graph
One of the Optimal
Solutions
The least number of discontinuities is 1
(note: the actual physical cutting
path is arbitrary.)

## Slide 27: Experiment : Polishing a “Hilly Terrain”
Going Through Discontinuity
First Section
Second Section

## Slide 28: Thanks for watching
Tong Yang, Jaime Valls Miro, Yue Wang, Rong Xiong
Robotic Laboratory, Zhejiang University
Centre for Autonomous Systems (CAS), University of Technology Sydney